## Slide 1: Adder Tree / MAC
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Energy Efficiency
TOPS/W drops from 0.65 to 0.33 with the increase of input toggle rate
  Tcycle = 2.6ns, 2.30 TOPS/mm2
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
TOPS/W | 0.65069 | 0.4149 | 0.34619 | 0.33057 | 0.35077

## Slide 3: Power of All Adder Tree Stages
Power of first few stages greatly depend on input toggle rate, while other stages do not
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.033232 | 0.094 | 0.16 | 0.222 | 0.285
ADD1 | 0.067278 | 0.162 | 0.217 | 0.246 | 0.235
ADD2 | 0.10827 | 0.197 | 0.245 | 0.23 | 0.17
ADD3 | 0.13698 | 0.20576 | 0.225 | 0.218 | 0.183
ADD4 | 0.12953 | 0.167 | 0.176 | 0.171 | 0.155
ADD5 | 0.11109 | 0.128 | 0.132 | 0.13 | 0.118
ADD6 | 0.070378 | 0.076 | 0.08 | 0.075 | 0.069

## Slide 4: Input Initial condition
The proportion of 0’s in first input pattern does not affect the power of MAC
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
50% | 1.1822 | 1.854 | 2.222 | 2.327 | 2.193
70% | 1.0374 | 1.8354 | 2.1978 | 2.3168 | 2.1903
90% | 1.0599 | 1.8979 | 2.1827 | 2.3304 | 2.1796

## Slide 5: Input Initial condition
The power distribution in all stages are same as 50% 0’s input pattern’s result
Chart: Input Toggle Rate(70% 0)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.032 | 0.092 | 0.161 | 0.219 | 0.284
ADD1 | 0.06 | 0.158 | 0.223 | 0.245 | 0.22
ADD2 | 0.094 | 0.199 | 0.24 | 0.229 | 0.171
ADD3 | 0.12 | 0.2 | 0.224 | 0.217 | 0.185
ADD4 | 0.111 | 0.162 | 0.167 | 0.175 | 0.16
ADD5 | 0.095 | 0.129 | 0.129 | 0.125 | 0.123
ADD6 | 0.061 | 0.077 | 0.073 | 0.074 | 0.071
Chart: Input Toggle Rate(90% 0)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.0328 | 0.102 | 0.161 | 0.223 | 0.288
ADD1 | 0.062 | 0.164 | 0.224 | 0.241 | 0.246
ADD2 | 0.096 | 0.207 | 0.232 | 0.228 | 0.167
ADD3 | 0.12 | 0.204 | 0.222 | 0.217 | 0.17
ADD4 | 0.112 | 0.168 | 0.175 | 0.179 | 0.151
ADD5 | 0.101 | 0.127 | 0.124 | 0.128 | 0.116
ADD6 | 0.063 | 0.079 | 0.071 | 0.076 | 0.07

## Slide 6: Timing diagram?
AND 7 mA
VDD1 3.5 mA
VDD2 1.6 mA
VDD3 1.2 mA
VDD4 0.7 mA
VDD5 0.9 mA
VDD6 0.3 mA

## Slide 7: Interleaved FA
Interleave 28T FAs along with 14T Fas
  30% smaller than the original design
  But require longer cycle time (2.9ns)
  Consumes 18% more power

## Slide 8: Interleaved FA
Chart: I (mA)
| AND | ADD1 | ADD2 | ADD3 | ADD4 | ADD5 | ADD6
28T | 0.15885 | 0.18546 | 0.19005 | 0.17901 | 0.15971 | 0.12382 | 0.074076
interleaved | 0.1868 | 0.1692 | 0.3214 | 0.17901 | 0.1802 | 0.0914 | 0.049
Energy Efficiency and Area Efficiency
  0.26 TOPS/W, 2.97 TOPS/mm2
Interleaved FA structure consumes more power in most stages

## Slide 9: Interleaved FA
AND 6(7) mA
VDD1 2(3.5) mA
VDD2 0.8(1.6) mA
VDD3 0.6(1.2) mA
VDD4 0.7(0.7) mA
VDD5 0.5(0.9) mA
VDD6 0.15(0.3) mA

## Slide 10: FA Sizing
High Vth for first few stages
  But I don’t know how to modify Vth
Design first few stages smaller and last 2 stages larger
  Alternative approach
  May require more area

## Slide 11: FA Sizing
Energy efficiency
  0.26 -> 0.29 TOPS/W
Area efficiency
  2.97 -> 2.81 TOPS/mm2

## Slide 12: FA Sizing
AND 1.8(6) mA
VDD1 0.7(2) mA
VDD2 0.1(0.8) mA
VDD3 0.8(0.6) mA
VDD4 0.8(0.7) mA
VDD5 0.6(0.5) mA
VDD6 0.6(0.15) mA

## Slide 13: FA Sizing
Apply on the original design
Energy efficiency
  0.33 -> 0.36 TOPS/W
Area efficiency
  2.30 -> 1.27 TOPS/mm2
  Since minimum width is 250nm, increase L to lower drain current -> more area -> bad result

## Slide 14: Adder Tree
Calculate 64 1-bit input with groups of 2 input adders
  Why not use multiple input adder
Carry save adder design

## Slide 15: Carry Save Adder Tree
For regular 64b to 6b adder tree
  Require 120 Full adders
  Ripple carry adders propagate carries in every stage
  Long critical path
Carry save adder design
  Only 64 full adders is used
  Only need to propagate delay in the last stage
  Relatively short critical path

## Slide 16: Performance
0.45 TOPS/W
  36% improvement w.r.t. the original design
4.49 TOPS/mm2
  95% improvement w.r.t. the original design
2.3 ns cycle time
  15% less than the original design
Chart: Power (mW)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
 | 0.772 | 1.2766 | 1.4696 | 1.701 | 1.9403
Chart: 
| AND | ADD1 | ADD2 | ADD3 | ADD4 | ADD5 | ADD6 | ADD7 | ADD8
 | 0.033 | 0.061 | 0.071 | 0.07 | 0.061 | 0.039 | 0.038 | 0.028 | 0.023
 | 0.106 | 0.14 | 0.114 | 0.095 | 0.083 | 0.052 | 0.051 | 0.035 | 0.029
 | 0.168 | 0.178 | 0.121 | 0.093 | 0.083 | 0.049 | 0.048 | 0.04 | 0.032
 | 0.242 | 0.213 | 0.139 | 0.102 | 0.087 | 0.056 | 0.054 | 0.039 | 0.03
 | 0.308 | 0.27 | 0.171 | 0.116 | 0.101 | 0.064 | 0.059 | 0.041 | 0.032

## Slide 17: CSA Tree with interleaving
1st stage: 14T, 2nd stage: 28T ……
  But ensure output are driven by 28T FA
  37/64 FAs are replaced by 14T FA
Performance gets better!
  0.54 TOPS/W, 4.70 TOPS/mm2
Chart: 
| AND | ADD1 | ADD2 | ADD3 | ADD4 | ADD5 | ADD6 | ADD7 | ADD8
 | 0.082 | 0.086 | 0.113 | 0.051 | 0.103 | 0.027 | 0.054 | 0.022 | 0.027
 | 0.16 | 0.105 | 0.183 | 0.064 | 0.141 | 0.032 | 0.067 | 0.025 | 0.032
 | 0.224 | 0.101 | 0.212 | 0.061 | 0.142 | 0.027 | 0.064 | 0.023 | 0.029
 | 0.265 | 0.075 | 0.223 | 0.062 | 0.152 | 0.033 | 0.071 | 0.02 | 0.028
 | 0.291 | 0.028 | 0.23 | 0.055 | 0.143 | 0.066 | 0.023 | 0.024 | 0.024
Chart: Power (mW)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
 | 1.0272 | 1.4627 | 1.591 | 1.6195 | 1.6032