## Slide 1: Title
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Recall
  Dual-granularity cooperative quantizer
    When quantizing analog voltage, use another ckt to calculate an approximated result
Vs (MAC result)
High precision
Low precision
Total : N iterations
Total V : N(Vs/2)
Counter : N(Vs/2) / Vref

## Slide 3: Quantizing MAC Voltage
  Coarse-grained method
    Takes iterations to get n bit precision
    Area is roughly a fixed value
  SAR ADC
    Takes n iterations to get n bit precision
    Area is proportional to (dominated by caps)
0.01100011010 x VDD
8 x 32 x 8
Coarse-grained
Fine-grained

## Slide 4: Quantizing MAC Voltage
  Partition of coarse/fine grained result
    Suppose Vref=VDD
0.01100011010 x VDD
Coarse-grained
Fine-grained
After 16 iteration,
011.00011010 x VDD
011.00000000 x VDD
000.00011010 x VDD

## Slide 5: Quantizing MAC Voltage
  3-bit coarse, 8-bit fine
Bit precision can reach 11 bit in lossless situation

## Slide 6: Parasitic Effect
  Coarse-grained method is iterative
    Loss in each iteration accumulates
    ADC is also a source of noise
Coarse-grained loss (%)
AVG bit precision
ADC loss (%)
AVG bit precision

## Slide 7: Parasitic Effect
  Coarse-grained method is iterative
    Loss in each iteration accumulates
    ADC is also a source of noise
11 bit

## Slide 8: Effect of DGCQ
  ADC : Large area, larger loss
  Coarse-grained : Time-consuming
  Dual-granularity : Less area, low loss, fast
Best in general
Fine-Grained
Coarse-Grained
DGCQ

## Slide 9: Effect of DGCQ on ML Tasks
  The dataset used in the paper is ImageNet
    ImageNet is not implemented in torch
    Use a simpler dataset CIFAR-10
  ResNet-18
    Trained using fp precision
    Quantize to int8 after training
    Compute MAC result for each layer and apply loss
-LOSS
Gaussian(-Loss,0.01)

## Slide 10: Effect of DGCQ on ML Tasks
  Comparison between coarse/fine-grained value
Fine-Grained
Coarse-Grained
DGCQ
DGCQ : Merge 2 types of granularity