## Slide 1: A 28nm 64kb Bit-Rotated Hybrid-CIM Macro with an Embedded Sign-Bit-Processing Array and a Multi-Bit-Fusion Dual-Granularity Cooperative Quantizer
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Motivation & Challenge
  Hybrid CIM
    Balance between DCIM and ACIM
    Challenge1 : definition problem of boundary between digital and analog part
    Challenge2 : more expensive overhead of sign-bit processing on digital part
    Challenge3 : energy wasted on low-accuracy-contributed quantization on analog part

## Slide 3: CIM Macro

## Slide 4: Proposed Scheme
  Bit-rotated feature-in scheme
    Low hardware overhead as bit-serial
    High accuracy as bit-parallel

## Slide 5: Proposed Scheme
  Embedded sign-bit-processing hybrid array

## Slide 6: Proposed Scheme
  Multi-bit-fusion
  Coarse/fine-grained quantizer

## Slide 7: Results
  Low accuracy loss but great energy reduction
    4-times readout combination incurs almost no accuracy loss and outperforms 5/6-times readout combinations regarding energy consumption

## Slide 8: Results
  MF-DGCQ achieves 24% performance enhancement and 4.27× power reduction with relative error of 3.57% in TT corner

## Slide 9: Results
  This design outperforms typical bit-parallel / serial work on the FoM (area efficiency × energy efficiency) by 15.7× and 3.38×.
  Accuracy loss -1.06% for ResNet-18@ImageNet, -1.75% for ViT@ImageNet, 0.19 for GPT-2@Wikitext-102.

## Slide 10: Results
  21.04TOPS/W@0.9V, 1.57TOPS/mm2@0.9V.
  Access time is 12ns@0.9V, 8bIN–8bW–21bOUT.