## Slide 1: Adder Tree / MAC
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Energy Efficiency
TOPS/W drops from 0.65 to 0.33 with the increase of input toggle rate
  Tcycle = 2.6ns, 2.30 TOPS/mm2
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
TOPS/W | 0.65069 | 0.4149 | 0.34619 | 0.33057 | 0.35077

## Slide 3: Power of All Adder Tree Stages
Power of first few stages greatly depend on input toggle rate, while other stages do not have obvious dependencies
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.033232 | 0.094 | 0.16 | 0.222 | 0.285
ADD1 | 0.067278 | 0.162 | 0.217 | 0.246 | 0.235
ADD2 | 0.10827 | 0.197 | 0.245 | 0.23 | 0.17
ADD3 | 0.13698 | 0.20576 | 0.225 | 0.218 | 0.183
ADD4 | 0.12953 | 0.167 | 0.176 | 0.171 | 0.155
ADD5 | 0.11109 | 0.128 | 0.132 | 0.13 | 0.118
ADD6 | 0.070378 | 0.076 | 0.08 | 0.075 | 0.069

## Slide 4: Input Initial condition
Chart: Input Toggle Rate(90% 0s initially)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.0328 | 0.102 | 0.161 | 0.223 | 0.288
ADD1 | 0.062 | 0.164 | 0.224 | 0.241 | 0.246
ADD2 | 0.096 | 0.207 | 0.232 | 0.228 | 0.167
ADD3 | 0.12 | 0.204 | 0.222 | 0.217 | 0.17
ADD4 | 0.112 | 0.168 | 0.175 | 0.179 | 0.151
ADD5 | 0.101 | 0.127 | 0.124 | 0.128 | 0.116
ADD6 | 0.063 | 0.079 | 0.071 | 0.076 | 0.07
The power distribution in all stages are same as 50% 0’s input pattern’s result
Chart: Input Toggle Rate(70% 0s initially)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.032 | 0.092 | 0.161 | 0.219 | 0.284
ADD1 | 0.06 | 0.158 | 0.223 | 0.245 | 0.22
ADD2 | 0.094 | 0.199 | 0.24 | 0.229 | 0.171
ADD3 | 0.12 | 0.2 | 0.224 | 0.217 | 0.185
ADD4 | 0.111 | 0.162 | 0.167 | 0.175 | 0.16
ADD5 | 0.095 | 0.129 | 0.129 | 0.125 | 0.123
ADD6 | 0.061 | 0.077 | 0.073 | 0.074 | 0.071

## Slide 5: Input Initial condition
The proportion of 0’s in first input pattern does not affect the power of MAC
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
50% | 1.1822 | 1.854 | 2.222 | 2.327 | 2.193
70% | 1.0374 | 1.8354 | 2.1978 | 2.3168 | 2.1903
90% | 1.0599 | 1.8979 | 2.1827 | 2.3304 | 2.1796

## Slide 6: Timing diagram?
AND 7 mA
VDD1 3.5 mA
VDD2 1.6 mA
VDD3 1.2 mA
VDD4 0.7 mA
VDD5 0.9 mA
VDD6 0.3 mA

## Slide 7: Interleaved FA
Interleave 28T FAs along with 14T Fas
  30% smaller than the original design
  But require longer cycle time (2.9ns)
  Consumes 18% more power in average

## Slide 8: Interleaved FA
Chart: I (mA)
| AND | ADD1 | ADD2 | ADD3 | ADD4 | ADD5 | ADD6
28T | 0.15885 | 0.18546 | 0.19005 | 0.17901 | 0.15971 | 0.12382 | 0.074076
interleaved | 0.1868 | 0.1692 | 0.3214 | 0.17901 | 0.1802 | 0.0914 | 0.049
Energy Efficiency and Area Efficiency
  0.26 TOPS/W, 2.97 TOPS/mm2
Interleaved FA structure consumes more power in most stages

## Slide 9: Interleaved FA
AND 6(7) mA
VDD1 2(3.5) mA
VDD2 0.8(1.6) mA
VDD3 0.6(1.2) mA
VDD4 0.7(0.7) mA
VDD5 0.5(0.9) mA
VDD6 0.15(0.3) mA

## Slide 10: FA Sizing
High Vth for first few stages
  But I don’t know how to modify Vth
Design first few stages smaller and last 2 stages larger
  Alternative approach
  May require more area

## Slide 11: FA Sizing
Applied on the interleaved design
  Energy efficiency: 0.26 -> 0.29 TOPS/W
  Area efficiency: 2.97 -> 2.81 TOPS/mm2
Slight improvement on energy efficiency
  Area efficiency dropped, but not much

## Slide 12: FA Sizing
AND 1.8(6) mA
VDD1 0.7(2) mA
VDD2 1(0.8) mA
VDD3 0.8(0.6) mA
VDD4 0.8(0.7) mA
VDD5 0.6(0.5) mA
VDD6 0.6(0.15) mA

## Slide 13: FA Sizing
Apply on the original design
Energy efficiency
  0.33 -> 0.36 TOPS/W
Area efficiency
  2.30 -> 1.27 TOPS/mm2
  Since minimum width is 250nm, increase L to lower drain current -> more area -> bad result

## Slide 14: Adder Tree
Calculate 64 1-bit input with groups of 2 input adders
  FA has 3 degree of freedom at input but we only utilize 2 of them
  We should use the FA fully
Carry save adder design
  Multiple input

## Slide 15: Adder Tree

## Slide 16: Carry Save Adder Tree
For regular 64b to 6b adder tree
  Require 120 Full adders
  Ripple carry adders propagate carries in every stage
  Long critical path
Carry save adder design
  Only 67 full adders is used
  Only need to propagate delay in the last stage
  Relatively short critical path

## Slide 17: CSA Tree Performance
0.45 TOPS/W
  36% improvement w.r.t. the original design
4.33 TOPS/mm2
  88% improvement w.r.t. the original design
2.3 ns cycle time
  15% less than the original design
Chart: Power (mW)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
 | 0.772 | 1.2766 | 1.4696 | 1.701 | 1.9403
Chart: 
| AND | ADD1 | ADD2 | ADD3 | ADD4 | ADD5 | ADD6 | ADD7 | ADD8
 | 0.033 | 0.061 | 0.071 | 0.07 | 0.061 | 0.039 | 0.038 | 0.028 | 0.023
 | 0.106 | 0.14 | 0.114 | 0.095 | 0.083 | 0.052 | 0.051 | 0.035 | 0.029
 | 0.168 | 0.178 | 0.121 | 0.093 | 0.083 | 0.049 | 0.048 | 0.04 | 0.032
 | 0.242 | 0.213 | 0.139 | 0.102 | 0.087 | 0.056 | 0.054 | 0.039 | 0.03
 | 0.308 | 0.27 | 0.171 | 0.116 | 0.101 | 0.064 | 0.059 | 0.041 | 0.032

## Slide 18: CSA Tree with interleaving
1st stage: 14T, 2nd stage: 28T ……
  But ensure output are driven by 28T FA
  37/67 FAs are replaced by 14T FA
Performance
  0.43 TOPS/W, 4.47 TOPS/mm2
Chart: 
| AND | ADD1 | ADD2 | ADD3 | ADD4 | ADD5 | ADD6 | ADD7 | ADD8
 | 0.082 | 0.086 | 0.113 | 0.051 | 0.103 | 0.027 | 0.054 | 0.022 | 0.027
 | 0.16 | 0.105 | 0.183 | 0.064 | 0.141 | 0.032 | 0.067 | 0.025 | 0.032
 | 0.224 | 0.101 | 0.212 | 0.061 | 0.142 | 0.027 | 0.064 | 0.023 | 0.029
 | 0.265 | 0.075 | 0.223 | 0.062 | 0.152 | 0.033 | 0.071 | 0.02 | 0.028
 | 0.291 | 0.028 | 0.23 | 0.055 | 0.143 | 0.066 | 0.023 | 0.024 | 0.024
Chart: Power (mW)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
 | 1.0272 | 1.4627 | 1.591 | 1.6195 | 1.6032

## Slide 19: CSA Tree with inverting FA
More than better
Use inverting full adders to remove the redundant inverters in FA’s output stage
  28T -> 24T
  May require extra inverters in some stages and at output
  Driving capability of FA may drop due to no buffer at output
  Saves some time consumed by INVs but smaller drain currents require more time to charge nodes
FA
A
B
FA
C

## Slide 20: Performance of CSA Tree w/ invFA
0.55 TOPS/W, 5.14 TOPS/mm2
  22% improvement in energy efficiency
  15% improvement in area efficiency
  Cycle time = 2.3 ns
What about the design with interleaving
  0.51 TOPS/W, 5.35 TOPS/mm2
  19% improvement in energy efficiency
  19% improvement in area efficiency
  Cycle time = 2.9ns

## Slide 21: Summary of All Designs
Adder Type | Additional Feature | Energy Efficiency | Area Efficiency | Cycle Time
Ripple Carry | No | 0.33 | 2.30 | 2.6
Ripple Carry | Interleaving | 0.26 | 2.97 | 2.9
Ripple Carry | Sizing | 0.36 | 1.27 | 2.7
Ripple Carry | Interleaving Sizing | 0.29 | 2.81 | 3.0
Carry Save | No | 0.45 | 4.33 | 2.3
Carry Save | Interleaving | 0.43 | 4.47 | 2.9
Carry Save | Inverting | 0.55 | 5.14 | 2.3
Carry Save | Interleaving Inverting | 0.51 | 5.35 | 2.9

## Slide 22: Summary
Ripple carry adder tree
  Longer delay, large area, and higher power
  Easy to implement and debug
  Compatible with input size scaling
Carry save adder tree
  Shorter delay, small area, and lower power
  Hard to implement and debug
  Cannot be made to be compatible with input size scaling easily (I don’t know how to)
Maybe even better?
  Use abc+yosys to further optimize adder tree

## Slide 23: Summary
Standard (do nothing)
  Old friends are always reliable
Interleaving
  Energy efficiency + Speed <-> Area efficiency
Vth scaling Transistor Sizing
  As pathetic as my electric circuit design grade
Inverting Full Adders
  Increasing both energy and area efficiency
  Very very good idea