## Slide 1: Noise Margin
B11901027 王仁軒

## Slide 2: Procedure
Hspice simulation
Download data
Post-processing done by python
  Rotate the curves ccw by 45 degree
  Subtract two curves
  Find min(local maximum, -local minimum) for SNM, RNM
  Find local maximum (or global maximum) for WNM

## Slide 3: SNM (corners)
Best at SF, worst at FF
TT
0.562
SS
0.634
SF
0.647
FS
0.590
FF
0.526

## Slide 4: SNM (supply voltage)
Roughly linear to VDD
  At TT
Chart: SNM-V
| 0.9 | 1.2 | 1.8
Y 值 | 0.366 | 0.456 | 0.562

## Slide 5: SNM (width)
Noise margin with Wn or Wp
  VDD = 1.8 V
Wp = 0.25 um
0.533
Wp = 0.35 um
0.569
Wn = 0.82 um
0.560
Wn = 0.62 um
0.564
Wn = 0.72 um
Wp = 0.30 um
0.562

## Slide 6: RNM (corners)
Best at SF, worst at FF
TT
0.214
SS
0.283
SF
0.350
FS
0.241
FF
0.170

## Slide 7: RNM (supply voltage)
NM with VDD
  At TT
Chart: SNM-V
| 0.9 | 1.2 | 1.8
Y 值 | 0.165 | 0.198 | 0.214

## Slide 8: RNM (width)
Noise margin with Wn or Wp
  VDD = 1.8 V
Wp = 0.24 um
0.196
Wp = 0.36 um
0.216
Wn = 0.84 um
0.237
Wn = 0.60 um
0.167
Wn = 0.72 um
Wp = 0.30 um
0.214

## Slide 9: WNM (corners)
Best at FF, worst at FS
TT
0.790
SS
0.644
SF
0.637
FS
0.628
FF
0.794

## Slide 10: WNM (supply voltage)
Roughly linear to VDD
  At TT
Chart: SNM-V
| 0.9 | 1.2 | 1.8
Y 值 | 0.377 | 0.473 | 0.79

## Slide 11: WNM (width)
Noise margin with Wn or Wp
  VDD = 1.2 V
Wn = 0.72 um
Wp = 0.30 um
0.473
Wp = 0.25 um
0.472
Wp = 0.36 um
0.473
Wn = 0.84 um
0.471
Wn = 0.60 um
0.475

## Slide 12: WNM
Some special cases
monotonic