## Slide 1: 2021
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Motivation & Background
  ML computing is data-centric
    Energy in Traditional Von Neumann structure is mainly consumed by memory accesses
    Computation in memory tackles this problem
  CIM structures focus on analog approach more
    Analog designs lack accuracy (SNR )
    Using digital structures can guarantee accuracy, also good for operations such as batch-norm, pooling
INPUT
OUTPUT
ALU
Memory

## Slide 3: Features
  High bit-flexibility
    Programmable bit-widths, signed/unsigned, and weights with 4, 8, 12, 16 bit widths..
  Parallel MAC operations, with high energy/area efficiency and throughput

## Slide 4: Structure
  2 Mode: SRAM & CIM
    SRAM: update weight
    CIMW: MAC operation, support 256×64 multiplication

## Slide 5: Structure
  2 Mode: SRAM & CIM
    SRAM: update weight
    CIMW: MAC operation , support 256×64 multiplication
  Require 5 cycles for
  4-bit input activation

## Slide 6: Structure
  Dynamic voltage scaling
    0.8V for weight updating
    0.68V for MAC operation
    Better NM and less dynamic power
  Interleaved 28T & 14T Adder
    Lower dynamic power

## Slide 7: Structure
  Update weight and perform MAC simultaneously
    When input = 0, Update weight
  Flexible bit width
    Separate 16 bit into 4b signed And 3×4b unsigned

## Slide 8: Result
  89TOPS/W under 0.72V for a sparse pattern
    (18% input toggle rate, 50% 1s for weights)
  52TOPS/W for a dense pattern
    (50% input toggle rate, 50% 1s for weights)
  3.3TOPS from 0.72V at 25°C
    TOPS/W and TOPS/area improving by 2.8× and 19× under 5nm process compared to 22nm design

## Slide 9: Conclusion
  Full precision
    Digital adder tree structure with 256×64 bit sram array
  Low power
    Dynamic voltage scaling ( lower VDD for MAC )
    Half of the 28T adders are replaced by 14T adders
  Highly programmable
    Support different input bit-width and weight bit-width
    Requires extra adder for sign extension and control blocks

## Slide 10: 2022
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 11: Motivation & Background
  Accuracy and scale of analog approach is limited
    MOS PVT variation
    ADC output range under dynamic voltage scaling
    Truncation and gain error of ADC
    Nonlinear Id due to drain-induced-barrier-lowering for current-based approach (lower Vt for short channel)
    Smaller caps with technology-scaling for cap-approach
    Analog components are not good for testing

## Slide 12: Motivation & Background
  Digital approach achieves better performance
    >1.3× power efficiency
    >1.4× performance/area efficiency

## Slide 13: Features
  Allows simultaneous MAC and write operations
  Small area
  Low power
  Flexible bit width
    4b, 8b, … weight and input

## Slide 14: Structure
  64 MAC arrays with 64kb of 12T sram cell
  64 banks, each bank contains 4b×4b

## Slide 15: Structure
  Read operations reads data from the cell to NOUT
  Accumulator/Adder does sign extension if needed
    Can support 8b data

## Slide 16: Structure
  Inverse FA
    12.5% smaller area, 15 % less total MAC power
    FA(, , ) = (, )

## Slide 17: Structure
  Place adder closer to sram cell
    Easier for routing
    Shorter wire
  Merge 12T sram with logic part
    No dummy space for transition region between sram/add
    Space can be less than 6T sram design

## Slide 18: Structure
  Interleaved write WL
    Easier for routing in y-direction
  Shared Read WL
    Easier for routing in x-direction

## Slide 19: Structure
  No RBL precharge
    CMOS output of 12 T sram does not need precharge
    Saves power

## Slide 20: Structure
  Update weight when MAC is not using the cell
    Time of updating can be faster than MAC if faster clock for write operation is used

## Slide 21: Result
  Area: 12208 μm2
    3× smaller than using a similar digital architecture
  Vmin: 0.5V at −40°C with a 95% yield.
  Fmax: 0.36, 0.96, 1.44GHz at 0.5, 0.7, 0.9V

## Slide 22: Result
  TOPS/W vs TOPS/mm2 chart:
    VDD = 0.5 V ~ 0.9V
    253.5, 205.0 and 155.2TOPS/W with 10, 25 and 50% input bit sparsity under 0.5 V

## Slide 23: Conclusion
  Allows simultaneous MAC and write operations
    Update weight while not used for MAC
    Use a faster clock for updating
  Small area
    12T sram is better than 6T sram
    Inversed FA
    Shared WL/ interleaved WL
  Low power
    12T sram does not need BL precharge
    Inversed FA
  Flexible bit width
    Additional shift and add control