## Slide 1: AND / FA
B11901027 王仁軒

## Slide 2: NM with Wa Variation
SNM:
  Noise margin does not changewith Wa
RNM:
  Noise margin with Wa
WNM
  Noise margin with Wa
Wa = 0.48 um
0.794
Wa = 0.36 um
0.794
Wa = 0.60 um
0.794
Wa = 0.48 um
0.291
Wa = 0.36 um
0.373
Wa = 0.60 um
0.222
Wa = 0.48 um
0.473
Wa = 0.36 um
0.467
Wa = 0.60 um
0.475

## Slide 3: AND
Fastest at FF, slowest at SS
No Sizing -> rise time = 2x fall time
Chart: 1.8V Performance
| rise time | fall time | delay
SS | 144 | 63 | 178
SF | 68.9 | 52.8 | 127
TT | 56.7 | 28.5 | 73
FS | 55.7 | 30 | 76.8
FF | 46.3 | 24.5 | 59.5

## Slide 4: AND
Delay: FS > SF
  Unbalanced size -> maximum delay at falling
Chart: 1.8V Performance
| rise time | fall time | delay
SS | 144 | 63 | 178
SF | 68.9 | 52.8 | 127
TT | 56.7 | 28.5 | 73
FS | 55.7 | 30 | 76.8
FF | 46.3 | 24.5 | 59.5

## Slide 5: AND
High VDD -> Faster
Chart: Delay of VDD variation
| SS | SF | TT | FS | FF
1.8V | 178 | 127 | 73 | 76.8 | 59.5
1.2V | 355 | 234 | 125 | 134 | 96.2
0.9V | 785 | 482 | 220 | 234 | 155

## Slide 6: AND (Adjust W by 40%)
Adjust Wn,nand
Adjust Wp,nand
Chart: 
| rise time | fall time | delay
wn*1.4 | 55.1 | 29.7 | 64.9
TT | 56.7 | 28.5 | 73
wn/1.4 | 59.9 | 27.3 | 84
Chart: 
| rise time | fall time | delay
wp*1.4 | 58.9 | 26.7 | 79
TT | 56.7 | 28.5 | 73
wp/1.4 | 57.1 | 29.9 | 69

## Slide 7: AND (Adjust W by 40%)
Adjust Wn,inv
Adjust Wp,inv
Chart: 
| rise time | fall time | delay
wn*1.4 | 60.9 | 27.2 | 79
TT | 56.7 | 28.5 | 73
wn/1.4 | 54.9 | 32.3 | 68.7
Chart: 
| rise time | fall time | delay
wp*1.4 | 52.2 | 29.8 | 70.8
TT | 56.7 | 28.5 | 73
wp/1.4 | 65.3 | 27.9 | 77.3

## Slide 8: 28T Full Adder
Structure
  Cout = MAJ(A , B , Cin)
  Sum = ABC + (A + B + Cin)
  Wp = 0.75u, Wn = 0.25u

## Slide 9: 28T Full Adder
Fastest at FF, slowest at SS
Chart: 1.8V Performance
| rise time | fall time | max delay | min delay
SS | 148 | 155 | 639 | 259
SF | 111 | 117 | 416 | 182
TT | 66.5 | 61.6 | 263 | 91.1
FS | 67.4 | 66.1 | 259 | 101
FF | 57.1 | 53.3 | 218 | 70

## Slide 10: 28T Full Adder
High VDD -> Faster
Chart: Delay of VDD variation
| SS | SF | TT | FS | FF
1.8V | 639 | 416 | 263 | 259 | 218
1.2V | 1290 | 783 | 457 | 451 | 352
0.9V | 2860 | 1650 | 855 | 839 | 595

## Slide 11: 28T Full Adder
Critical path
  A: 1->0 , B: 1 , Cin: 0, Cout: 1->0, Sum: 0->1

## Slide 12: 28T Full Adder
Critical path
  A: 1->0 , B: 1 , Cin: 0, Cout: 1->0, Sum: 0->1
  Delay can be estimated by Elmore RC model
  Longer path -> larger effective capacitance

## Slide 13: 28T Full Adder (Adjsut W by 40%)
Adjust Wn (excluding inverters)
Adjust Wp (excluding inverters)
  Shorter delay when reducing size of Wp
  Max/Min delay happens at Sum : 0 -> 1
Chart: Wn,nand
| rise time | fall time | max delay | min delay
wn*1.4 | 64.1 | 67.1 | 249 | 79.9
TT | 66.5 | 61.6 | 263 | 91.1
wn/1.4 | 88.4 | 60.5 | 304 | 119
Chart: Wn,nand
| rise time | fall time | max delay | min delay
wp*1.4 | 78.1 | 62.1 | 278 | 107
TT | 66.5 | 61.6 | 263 | 91.1
wp/1.4 | 64.9 | 69.2 | 261 | 77.5