## Slide 1: CIM
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Outline
Analog vs Digital
Analog CIM structure
  Optimization techniques for analog designs
Digital CIM structure
  Optimization techniques for digital designs
Overall comparison among 3 papers

## Slide 3: Analog CIM Structure
Multiply input with weight
(n-bit) (1-b)
Sum of all partial products
Typical analog CIM Structure
  Require DAC & ADC

## Slide 4: Optimization for Analog Designs
Analog multiplication requires DAC
  Current source may consume lots of power
Not using DAC
  Digital multiplication
Differential output
Current source are always on
Single-ended output
Can turn off current source
Input_B
Weight(QB)
1-bit partial sum
Require shift and sum
to do n-bit x n-bit
from 1-bit x 1-bit

## Slide 5: Optimization for Analog Designs
ADC is required
Reuse of Capacitors
Capacitance
Large area for caps
Reuse of caps for ADC allows us to save area

## Slide 6: Optimization for Analog Designs
Skipping iterations
Interleaving (memory cell)
Input has 32 1’s
Partial sum < 32
Skip first few iterations
saves time
sram
sram
sram
sram
sram
sram
sram
sram
RBL length = L
Parasitic caps = C
RBL length = L/2
Parasitic caps = C/2
RBL
RBL

## Slide 7: Digital CIM Structure
Typical digital CIM design
  Serial input
Digital multiplication
(1b input x 4b weight)
Adder tree to sum
all partial sums

## Slide 8: Optimization for Digital Designs
Increase throughput
  Increase input BW
High BW input memory
  In order to support MAC pipeline
Serial input
Require bit-precision+1 cycles
Parallel input
Require bit-precision/4+1 cycles

## Slide 9: Optimization for Digital Designs
Bit-flexibility & Adder tree optimization
Each color is produced by a CIM block
Do not propagate carry
Faster than ripple-carry tree

## Slide 10: Overall Comparison
 | 2021/Analog | 2023/Analog | 2022/Digital
Throughput TOPS (1b x 1b) | 1.30 | 1.31 | 98.3
Energy Efficiency TOPS/W (1b x 1b) | 293 | 291 | 625
Area Efficiency TOPS/mm2 (1b x 1b) | 23.01 | 27.7 | 10.49
Parallel input
Freq increase
Pipelining
ADC?
Adder tree
DAC