## Slide 1: 2021 / 2022
B11901027 王仁軒

## Slide 2: Motivation & Background
  ML computing is data-centric
    Energy in Traditional Von Neumann structure is mainly consumed by memory accesses
    Computation in memory tackles this problem
  CIM structures focus on analog approach more
    Analog designs lack accuracy (SNR )
    Using digital structures can guarantee accuracy, also good for operations such as batch-norm, pooling
INPUT
OUTPUT
ALU
Memory

## Slide 3: Features
  High bit-flexibility
    Programmable bit-widths, signed/unsigned, and weights with 4, 8, 12, 16 bit widths..
  Parallel MAC operations, with high energy/area efficiency and throughput

## Slide 4: Structure
  2 Mode: SRAM & CIM
    SRAM: update weight
    CIMW: MAC operation, support 256×64 multiplication

## Slide 5: Structure
  2 Mode: SRAM & CIM
    SRAM: update weight
    CIMW: MAC operation , support 256×64 multiplication
  Require 5 cycles for
  4-bit input activation

## Slide 6: Structure
  Dynamic voltage scaling
    0.8V for weight updating
    0.68V for MAC operation
    Better NM and less dynamic power
  Interleaved 28T & 14T Adder
    Lower dynamic power

## Slide 7: Structure
  Update weight and perform MAC simultaneously
    When input = 0, Update weight
  Flexible bit width
    Separate 16 bit into 4b signed And 3×4b unsigned

## Slide 8: Result
  89TOPS/W under 0.72V for a sparse pattern
    (18% input toggle rate, 50% 1s for weights)
  52TOPS/W for a dense pattern
    (50% input toggle rate, 50% 1s for weights)
  3.3TOPS from 0.72V at 25°C
    TOPS/W and TOPS/area improving by 2.8× and 19× under 5nm process compared to 22nm design

## Slide 9: Conclusion
  Full precision
    Digital adder tree structure with 256×64 bit sram array
  Low power
    Dynamic voltage scaling ( lower VDD for MAC )
    Half of the 28T adders are replaced by 14T adders
  Highly programmable
    Support different input bit-width and weight bit-width
    Requires extra adder for sign extension and control blocks