## Slide 1: Adder Tree / MAC
B11901027 王仁軒
PPT TemplateCredit : Jie-Hong Roland Jiang

## Slide 2: Energy Efficiency
TOPS/W drops from 0.65 to 0.33 with the increase of input toggle rate
  VDD = 1.8V
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
TOPS/W | 0.65069 | 0.4149 | 0.34619 | 0.33057 | 0.35077

## Slide 3: Power of All Adder Tree Stages
Power of first few stages greatly depend on input toggle rate, while other stages do not
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.033232 | 0.094 | 0.16 | 0.222 | 0.285
ADD1 | 0.067278 | 0.162 | 0.217 | 0.246 | 0.235
ADD2 | 0.10827 | 0.197 | 0.245 | 0.23 | 0.17
ADD3 | 0.13698 | 0.20576 | 0.225 | 0.218 | 0.183
ADD4 | 0.12953 | 0.167 | 0.176 | 0.171 | 0.155
ADD5 | 0.11109 | 0.128 | 0.132 | 0.13 | 0.118
ADD6 | 0.070378 | 0.076 | 0.08 | 0.075 | 0.069

## Slide 4: Input Initial condition
The proportion of 0’s in first input pattern does not affect the power of MAC
Chart: Input Toggle Rate
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
50% | 1.1822 | 1.854 | 2.222 | 2.327 | 2.193
70% | 1.0374 | 1.8354 | 2.1978 | 2.3168 | 2.1903
90% | 1.0599 | 1.8979 | 2.1827 | 2.3304 | 2.1796

## Slide 5: Input Initial condition
The power distribution in all stages are same as 50% 0’s input pattern’s result
Chart: Input Toggle Rate(70% 0)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.032 | 0.092 | 0.161 | 0.219 | 0.284
ADD1 | 0.06 | 0.158 | 0.223 | 0.245 | 0.22
ADD2 | 0.094 | 0.199 | 0.24 | 0.229 | 0.171
ADD3 | 0.12 | 0.2 | 0.224 | 0.217 | 0.185
ADD4 | 0.111 | 0.162 | 0.167 | 0.175 | 0.16
ADD5 | 0.095 | 0.129 | 0.129 | 0.125 | 0.123
ADD6 | 0.061 | 0.077 | 0.073 | 0.074 | 0.071
Chart: Input Toggle Rate(90% 0)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
AND | 0.0328 | 0.102 | 0.161 | 0.223 | 0.288
ADD1 | 0.062 | 0.164 | 0.224 | 0.241 | 0.246
ADD2 | 0.096 | 0.207 | 0.232 | 0.228 | 0.167
ADD3 | 0.12 | 0.204 | 0.222 | 0.217 | 0.17
ADD4 | 0.112 | 0.168 | 0.175 | 0.179 | 0.151
ADD5 | 0.101 | 0.127 | 0.124 | 0.128 | 0.116
ADD6 | 0.063 | 0.079 | 0.071 | 0.076 | 0.07

## Slide 6: Timing diagram?
AND
VDD1
VDD2
VDD3
VDD4
VDD5
VDD6

## Slide 7: Timing diagram?
AND
VDD1
VDD2
VDD3
VDD4
VDD5
VDD6